## Slide 1: FALA: Locality-Aware PIM-Host Cooperation for Graph Processing with Fine-Grained Column Access
Changmin Shin†, Jaeyong Song†, Seongmin Na†, Jun Sung†, Hongsun Jang†, Jinho Lee†
†: Seoul National University
The 58th IEEE/ACM International Symposium on Microarchitecture (MICRO)
MICRO 2025

## Slide 2: Introduction
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
Processing-in-Memory
…
Prefetch Buffer
Output Queue
NI
Processors
DRAM Bank
Graph Processing
(e.g., PageRank, BFS, …)
Random Memory Access
Memory Bottleneck
Cache-based Accelerator
e.g.) Graphicionado [MICRO’16], GraphDyns [MICRO’19], PolyGraph [ISCA’21]
PIM Accelerator
e.g.) Teserract [ISCA’15], GraphPIM [HPCA’17], GraphP [HPCA’18]

## Slide 3: Introduction: Existing Approaches
Burst Length: 32B
Memory Bandwidth Bottleneck
Difficult to Utilize Cache
Unnecessary Data Transfer
Processor Area Overheads
Processing-in-Memory
…
Prefetch Buffer
Output Queue
NI
Processors
DRAM Bank
Host Processor
Cores
Cache
IDLE
Vertex Data: ~8B
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
Memory
Data Cell Array
…
…
Cache-based Accelerator
e.g.) Graphicionado [MICRO’16], GraphDyns [MICRO’19], PolyGraph [ISCA’21]
PIM Accelerator
e.g.) Teserract [ISCA’15], GraphPIM [HPCA’17], GraphP [HPCA’18]

## Slide 4: Introduction: Existing Approaches
Processing-in-Memory
…
Prefetch Buffer
Output Queue
NI
Processors
DRAM Bank
Host Processor
Cores
Cache
IDLE
Burst Length: 32B
Vertex Data: ~8B
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
Memory
Data Cell Array
…
…
Cache? or PIM?
Cache-based Accelerator
e.g.) Graphicionado [MICRO’16], GraphDyns [MICRO’19], PolyGraph [ISCA’21]
PIM Accelerator
e.g.) Teserract [ISCA’15], GraphPIM [HPCA’17], GraphP [HPCA’18]
Memory Bandwidth Bottleneck
Difficult to Utilize Cache
Unnecessary Data Transfer
Processor Area Overheads

## Slide 5: Introduction: Design Goals
Processing-in-Memory
Accelerator and PIM
Co-Design of
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
FALA-PIM/CAS
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 15
FALA-PIM
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 0
…
…
…
1. Minimally Sized PIM
2. Fine-Grained Column Selection
PIM-Cache Cooperation Unit
Row Locality Monitor
3. Locality-Aware PIM Offloading

## Slide 6: Background and Motivation
Graph Processing with Accelerator
Introduction
Background
Motivation
FALA
Experiment Results
Conclusion

## Slide 7: Vertex-Centric Graph Processing
1
0
3
4
8
[1] Read Vertex Data
[2] Read Edge Data
[3] Process Each SrcProperty
[4] Update the DstProperty
1
3
0
1
4
1
8
1
4
3
e.g.) For SSSP: SrcProperty + EdgeWeight
e.g.) For SSSP: min(Result of [3], DstProperty)
: Vertex Property
(Src: , Dst: )

## Slide 8: Graph Processing with Accelerator
1
0
3
4
8
[1] Read Vertex Data
[2] Read Edge Data
[3] Process Each SrcProperty
[4] Update the DstProperty
1
3
0
1
4
1
8
1
4
3
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
Reduce Unit
…
Data Cell Array
Chip I/O
Memory
1
0
1
4
1
8
1

## Slide 9: Graph Processing with Accelerator
1
0
3
4
8
[1] Read Vertex Data
[2] Read Edge Data
[3] Process Each SrcProperty
[4] Update the DstProperty
1
3
0
1
4
1
8
1
4
3
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
Reduce Unit
…
Data Cell Array
Chip I/O
Memory
Update Destination Properties
1. Extremely Memory Bound
2. Unuseful Memory Access

## Slide 10: FALA
Memory-Side FALA Architecture
Host-Side FALA Architecture
Introduction
Background
Motivations
FALA
Experiment Results
Conclusion

## Slide 11: Overview of FALA
Processing-in-Memory
PIM-Cache Cooperation Unit
Row Locality Monitor
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
FALA-PIM/CAS
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 15
FALA-PIM
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 0
…
…
…
Accelerator
FALA-PIM Architecture
FALA-CAS Mechanism
Memory-Side FALA Architecture
PIM-Cache Cooperation Unit
Row Locality Monitor
Host-Side FALA Architecture

## Slide 12
WB Buf.
FALA-PIM: Architecture
HBM2 Bank w/ FALA-PIM
Subarrays (DRAM Cell Arrays)
Lightweight PIM with a simple single ALU
3-stage pipeline for updating destination properties
FALA-PIM
Column Decoder
Data Buffer
TSV
I/O
DATA
C/A
ALU
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
: Column Offset (Dst. ID)
: Processed SrcProperty
: DstProperty
0
4
8
RD Prop.
Update
WR Prop.
0
4
8
1
3
Δ0
Δ4
Δ8
Δ4

## Slide 13
ALU
Δ0
Δ4
Δ8
Δ4
WB Buf.
FALA-PIM: Execution Flow
HBM2 Bank w/ FALA-PIM
Subarrays (DRAM Cell Arrays)
Column offsets and source properties are sent via the data bus
A single PIM operation updates multiple destination vertices
FALA-PIM
Column Decoder
Data Buffer
TSV
I/O
DATA
C/A
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
: Column Offset (Dst. ID)
: Processed SrcProperty
: DstProperty
0
4
8
0
4
0
4
8
4
8
4
0
4
4
8
4
0
4
8
4
Δ0
Δ4
Δ8
Δ4
0
4
8
1
3
Δ0
Δ4
Δ8
Δ4

## Slide 14
TSV
I/O
DATA
C/A
FALA-PIM: Execution Flow
HBM2 pCH w/ FALA-PIM
Multiple banks within a pCH operate in parallel
Bank-level internal bandwidth can alleviate the memory bottleneck
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Bank Parallel Execution  Bandwidth Gain
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
WB Buf.
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
4

## Slide 15
TSV
I/O
DATA
C/A
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
0
4
8
4
WB Buf.
Subarrays (DRAM Cell Arrays)
FALA-PIM
Column Decoder
Data Buffer
ALU
0
4
8
4
Offset Buffer
Global Sense Amplifier
Data Hazard Resolver
0
4
8
4
The Need for Fine-Grained Access
HBM2 pCH w/ FALA-PIM
Fine-grained random access causes bandwidth waste
Both the host and PIM suffer from inefficient memory access
Unnecessary Data Transfer
Bank Parallel Execution  Bandwidth Gain
Need Fine-Grained Memory Access

## Slide 16
Conventional HBM2
A subarray is composed of multiple MATs.
HBM2 memory internal burst length = 2
Conventional HBM2 Bank
…
Row Dec.
Subarray
…
Column Decoder
Global Sense Amplifier
Column Decoder
DRAM CLK
Bank Access
Data Bus
32B Burst
32B Burst
16B
16B
16B
16B
16B
16B
16B
16B
32B Burst
32B Burst
: Unnecessary Data
: Target Data
16B Access
16B Access
CLK
Bank
Single Burst
All MATs operate in lock-step
32B burst (16B access per cycle)
4 Transactions for 4 Target Data
MAT

## Slide 17
In-Memory Scatter-Gather
In-memory scatter-gather through data buffer
Transfer only target data via off-chip bus
HBM2 Bank w/ In-Memory Scatter-Gather
…
Row Dec.
Subarray
…
Column Decoder
Global Sense Amplifier
Data Buff.
Offset Buff.
Column Decoder
DRAM CLK
Bank Access
Data Bus
32B Burst
32B Burst
16B
16B
16B
16B
16B
16B
16B
16B
16B Access
16B Access
CLK
Bank
Single Burst
: Column Offset
: Unnecessary Data
: Target Data
Still Inefficient in Bank Access
Piccolo: Large-Scale Graph Processing with Fine-Grained In-Memory Scatter-Gather [HPCA’25]

## Slide 18
8B Access
8B Access
CLK
Even
Odd
8B Access
8B Access
Single Burst
FALA-CAS: Architecture
Split the subarray into MatGroup w/ col. decoder
Access different column per MatGroup each cycle
HBM2 Bank w/ FALA-CAS
…
Row Dec.
Subarray
…
Global Sense Amplifier
Data Buff.
Offset Buff.
Column Decoder
Column Decoder
Even MatGroup
Odd MatGroup
DRAM CLK
Bank Access
Data Bus
32B Burst
32B Burst
8B
8B
8B
8B
: Column Offset
: Unnecessary Data
: Target Data
Access Only Necessary Data

## Slide 19: Design Goals
Processing-in-Memory
PIM-Cache Cooperation Unit
Row Locality Monitor
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
FALA-PIM/CAS
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 15
FALA-PIM
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 0
…
…
…
2. Fine-Grained Column Selection
1. Minimally Sized PIM ALU
3. Locality-Aware PIM Offloading
Cache
PIM-Host Cooperation
Accelerator and PIM
Co-Design of

## Slide 20: Locality-Aware PIM-Host Cooperation
Chart: Node Degree
Degree distribution of
real-world graph
Low-degree vertices
Most vertices: 1, 2 neighbors
Less opportunity for reuse
High-degree vertices
Few vertices: 10k~ neighbors
Exhibit high locality
PIM
Cache

## Slide 21: Locality-Aware PIM-Host Cooperation
Processing-in-Memory
PIM-Cache Cooperation Unit
Row Locality Monitor
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
FALA-PIM/CAS
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 15
FALA-PIM
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 0
…
…
…
Chart: Node Degree
Degree distribution of
real-world graph
1. Check the locality of the target data
2. Collect the memory requests
3. Issue the memory request
PIM Req
Req
Req
Req
Req
Req
Req
Req
READ

## Slide 22: Row Locality Monitor
Tag-only cache storing DRAM row addresses as tag
Row Locality Monitor
V
Partial DRAM Row Addr (Tag)
LRU
…
V
Partial DRAM Row Addr (Tag)
LRU
V
Partial DRAM Row Addr (Tag)
LRU
V
Row xx
Valid
DRAM Row Addr. (Tag)
LRU
Indexed by Row Addr.
If a row addr. hits  High Locality
If a row addr. misses  Low Locality
Processing-in-Memory
PIM-Cache Cooperation Unit
Row Locality Monitor
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
FALA-PIM/CAS
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 15
FALA-PIM
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 0
…
…
…

## Slide 23: PIM-Cache Cooperation Unit
Store req. type  PIM or Cache
Store req. info.  Col. Offset & Data
Collect memory requests that target the same row
PIM-Cache Cooperation Unit
Row xx
Type
Field
Col. Offset
Data
Req
Req
Req
Req
PIM/$
Indexed by Row Addr.
Processing-in-Memory
PIM-Cache Cooperation Unit
Row Locality Monitor
Accelerator
Prefetcher
Updater
Vertex
Prefetch
Processor
PE
S
I
M
D
…
…
…
UE
RA Unit
Edge
Prefetch
Cache
FALA-PIM/CAS
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 15
FALA-PIM
Global Sense Amplifier
Column Decoder
Column Decoder
Data Cell Array
Bank 0
…
…
…

## Slide 24: Overall Execution Flow (PIM Execution Flow)
v
Execution flow when data is determined low locality
2. Check for Monitor Hit
1. Check for
Cache Hit
3. Collect PIM Requests
4. Issue FALA-PIM Request
4’. Update Locality Information
FALA-PIM/FALA-CAS
Accelerator Core
Addr: Row yy, Col 4
PIM-Cache
Cooperation Unit
Row yy
…
Type
Field
PIM
Cache
Row Locality
Monitor
Row xx
…
Miss
Req
Req
Req
Req
Miss
Row yy
Req
FALA-PIM
Req

## Slide 25: Overall Execution Flow (Host Execution Flow)
v
Execution flow when data is determined high locality
2. Check for Monitor hit
1. Check for
Cache Hit
3. Collect Cache Requests
4. Issue FALA-CAS Request
4’. Update Locality Information
FALA-PIM/FALA-CAS
Accelerator Core
Addr: Row yy, Col 8
PIM-Cache
Cooperation Unit
Row yy
…
Type
Field
Cache
Cache
Row Locality
Monitor
Row yy
…
Hit
Req
Req
Req
Req
Miss
PIM
5. Send Read Data to Cache
Update
LRU
Req
FALA-CAS
Req

## Slide 26: Evaluation
Experimental Methodology
Evaluation Results
Introduction
Background
Motivations
FALA
Evaluation Results
Conclusion

## Slide 27: Experimental Methodology
3. Baselines
  GraphDyns: Cache-Only Acc.
  GraphPIM: PIM-Only Acc.
  PEI: Traditional Locality Monitor
  Piccolo: In-Memory Scatter-Gather
Objective | Component | Evaluation Method
Performance | Overall | Simulation
Energy and Area | Accelerator & DRAM Cache | RTL Synthesis CACTI
1. Method
2. Dataset
  5 large-scale graph dataset
  4 graph algorithms
  Use the best graph tiling config.
[HBM2 Memory Config.]
16pCH, 16 banks/pCH
256GB/s max. bandwidth

## Slide 28: Evaluation: Speedup
3.76x, 2.39x, 1.59x, 1.56x speedups over the baselines
Both Cache-only (GraphDyns) and PIM-only (GraphPIM) are not enough
Significantly better performance with low DRAM area overhead (3.1%)
Chart: Speedup
| UU | SW | TW | FS | PP | UU | SW | TW | FS | PP | UU | SW | TW | FS | PP | UU | SW | TW | FS | PP | PR | BFS | CC | SSSP | GM
GraphDyns | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GraphPIM (HBM2) | 1.5767 | 1.0556 | 0.16062 | 0.79014 | 0.72772 | 1.2016 | 2.5188 | 0.21509 | 0.92284 | 1.794 | 1.8581 | 2.1143 | 0.21061 | 0.96498 | 1.2476 | 1.1533 | 2.2591 | 0.22774 | 0.64219 | 1.1778 | 0.87797
PEI (HBM2) | 2.4423 | 1.0515 | 0.97837 | 0.97206 | 0.92759 | 1.3881 | 2.2265 | 0.98247 | 1.0831 | 1.6424 | 2.1356 | 1.9819 | 0.97967 | 1.1171 | 1.2041 | 1.3674 | 2.0749 | 0.98224 | 1.02 | 1.2101 | 1.3138
Piccolo | 1.7239 | 1.1457 | 0.89846 | 1.4386 | 1.0386 | 1.3266 | 1.9273 | 0.93097 | 1.7266 | 1.9809 | 1.5057 | 1.6979 | 0.911 | 1.6662 | 1.3281 | 1.1154 | 1.7774 | 0.95421 | 1.294 | 1.4032 | 1.3462
FALA | 3.0353 | 2.2069 | 1.0551 | 2.0402 | 1.8344 | 1.9182 | 3.7635 | 1.1733 | 2.3054 | 3.4285 | 2.9221 | 3.3549 | 1.1086 | 2.3332 | 2.5666 | 1.4944 | 3.3812 | 1.1642 | 1.7012 | 2.3981 | 2.0994
1.56x
3.8x

## Slide 29: Evaluation: Ablation
FALA-CAS reduces inefficient memory access within each bank
Locality-aware PIM-host cooperation further enhances the overall performance.
Chart: Speedup
| UU | SW | TW | FS | PP | UU | SW | TW | FS | PP | UU | SW | TW | FS | PP | UU | SW | TW | FS | PP | PR | BFS | CC | SSSP | GM
GraphPIM (HBM2) | 1.5767 | 1.0556 | 0.16062 | 0.79014 | 0.72772 | 1.2016 | 2.5188 | 0.21509 | 0.92284 | 1.794 | 1.8581 | 2.1143 | 0.21061 | 0.96498 | 1.2476 | 1.1533 | 2.2591 | 0.22774 | 0.64219 | 1.1778 | 0.87797
FALA (PIM) | 2.381 | 1.7374 | 0.32504 | 1.3814 | 1.294 | 1.5555 | 3.1748 | 0.39516 | 1.5565 | 2.6347 | 2.3908 | 2.7196 | 0.36736 | 1.5275 | 1.8341 | 1.5219 | 2.8743 | 0.40279 | 1.1147 | 1.7993 | 1.358
FALA (PIM+CAS) | 3.1465 | 2.065 | 0.57416 | 1.6809 | 1.5833 | 1.6547 | 3.347 | 0.46365 | 1.6861 | 2.8242 | 2.6098 | 2.8745 | 0.43067 | 1.6465 | 1.9673 | 1.6193 | 3.0204 | 0.47074 | 1.206 | 1.9255 | 1.5545
FALA | 3.0353 | 2.2069 | 1.0551 | 2.0402 | 1.8344 | 1.9182 | 3.7635 | 1.1733 | 2.3054 | 3.4285 | 2.9221 | 3.3549 | 1.1086 | 2.3332 | 2.5666 | 1.4944 | 3.3812 | 1.1642 | 1.7012 | 2.3981 | 2.0994

## Slide 30: Evaluation: Off-chip Memory Access
Chart: Normalized Memory Access
| GraphDyns | GraphPIM | PEI | Piccolo | FALA | GraphDyns | GraphPIM | PEI | Piccolo | FALA | GraphDyns | GraphPIM | PEI | Piccolo | FALA | GraphDyns | GraphPIM | PEI | Piccolo | FALA | GraphDyns | GraphPIM | PEI | Piccolo | FALA | UU | SW | TW | FS | PP
Graph Topology Access | 0.15759 | 0.15759 | 0.15759 | 0.15759 | 0.15759 | 0.1683 | 0.1683 | 0.1683 | 0.1683 | 0.1683 | 0.29865 | 0.29865 | 0.29865 | 0.29865 | 0.29865 | 0.14012 | 0.14012 | 0.14012 | 0.14012 | 0.14012 | 0.13625 | 0.13625 | 0.13625 | 0.13625 | 0.13625
Property Access | 0.75038 | 0.38493 | 0.32969 | 0.77689 | 0.18427 | 0.80966 | 0.26182 | 0.20508 | 0.17289 | 0.059802 | 0.69145 | 0.93063 | 0.23082 | 0.13641 | 0.085518 | 0.85272 | 0.27406 | 0.18834 | 0.27454 | 0.043615 | 0.85659 | 0.27773 | 0.20478 | 0.19845 | 0.054646
Apply | 0.092035 | 0.092035 | 0.092035 | 0.092035 | 0.092035 | 0.022038 | 0.022038 | 0.022038 | 0.022038 | 0.022038 | 0.0098995 | 0.0098995 | 0.0098995 | 0.0098995 | 0.0098995 | 0.0071604 | 0.0071604 | 0.0071604 | 0.0071604 | 0.0071604 | 0.007159 | 0.007159 | 0.007159 | 0.007159 | 0.007159
FALA-CAS accesses and transfers only the necessary vertex properties.
Locality-aware PIM offloading dramatically minimizes the data transfer.
Vertex Property Access
Graph Topology Access
Others

## Slide 31: Conclusion
FALA presents an accelerator–PIM co-design
Our approach leverages
  Lightweight Processing-in-Memory
  Fine-Grained Column Access
  Locality-Aware PIM-Host Cooperation
FALA maximizes the bandwidth utilization, achieving high performance

## Slide 32: Thank you.
Changmin Shin @ Seoul National University
Email: scm8432@snu.ac.kr