## Slide 1: Piccolo: Large-Scale Graph Processing with Fine-Grained In-Memory Scatter-Gather
Changmin Shin†, Jaeyong Song†, Hongsun Jang†, Dogeun Kim†, Jun Sung†, Taehee Kwon†,
Jae Hyung Ju†, Frank Liu‡, Yeonkyu Choi§, Jinho Lee†
†: Seoul National University
‡: Old Dominion University
§:Samsung Electronics
The 31th IEEE International Symposium on High-Performance Computer Architecture (HPCA)
HPCA 2025

## Slide 2: Introduction
Processing-in-Memory
…
Prefetch Buffer
Output Queue
NI
In-Order Core
Data Cell Array
Graph Processing
(e.g., PageRank, BFS, …)
Random Memory Access
Memory Bottleneck
Cache-based Accelerator
PIM Accelerator
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit

## Slide 3: Introduction: Existing Approaches
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit
Unnecessary Data Access
Cache-based Accelerator
PIM Accelerator
Unable to Utilize Locality
Memory
Data Cell Array
…
…
Burst Length: 64B
Vertex Data: ~8B
Host Processor
Cores
Cache
IDLE
Processing-in-Memory
…
Prefetch Buffer
Output Queue
NI
In-Order Core
Data Cell Array
Waste Cache Capacity
Significant Overhead

## Slide 4: Introduction: Existing Approaches
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit
Memory
Data Cell Array
…
…
Burst Length: 64B
Vertex Data: ~8B
Host Processor
Cores
Cache
IDLE
Processing-in-Memory
…
Prefetch Buffer
Output Queue
NI
In-Order Core
Data Cell Array
Cache? or PIM?
Cache Coherency
Unnecessary Data Access
Cache-based Accelerator
PIM Accelerator
Unable to Utilize Locality
Waste Cache Capacity
Significant Overhead

## Slide 5: Introduction: Overview
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit
Piccolo-Cache
Benefit from Locality
Co-Design
Accelerator and Function-in-Memory
Transfer Only Necessary Data
Offset Buffer
Data Cell Array
…
Piccolo Function-in-Memory
Ctrl
Utilize Internal Bandwidth
Low Area Overhead
Data Buffer

## Slide 6: Background and Motivation
Graph Processing with Accelerator
Introduction
Background
Motivation
Piccolo
Experiment Results
Conclusion

## Slide 7: Graph Processing with Accelerator
0
2
4
9
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit
…
Data Cell Array
Chip I/O
Memory
0
2
4
9

## Slide 8: Graph Processing with Accelerator
Accelerator
Prefetcher
Processor
Updater
Cache
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit
0
2
9
4
…
Data Cell Array
Chip I/O
Memory
Unuseful Memory Access
Unuseful Cache Utilization
(Unuseful data: / Useful data: )

## Slide 9: Piccolo
Piccolo Function-in-Memory
Piccolo Cache
Introduction
Background
Motivations
Piccolo
Experiment Results
Conclusion

## Slide 10: Overview of Piccolo
Accelerator
Prefetcher
Processor
Updater
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit
Piccolo-Cache
l
Piccolo Function-in-Memory
Function-in-Memory Architecture
Operation within DDR Standard
…
Offset Buffer
Data Cell Array
Piccolo Function-in-Memory
Ctrl.
Data Buffer
Data Cell Array
l
Fine-Grained Cache Architecture
Collection-Extended MSHR
(2) Piccolo Cache

## Slide 11
RD Buff.
WR Buff.
Piccolo-FIM: Architecture
Data Cell Array
Conventional DRAM
Column Decoder & Mux
RD Buff.
WR Buff.
Data Cell Array
DRAM w/ Piccolo-FIM
Data Buffer
Offset Buffer
Column Decoder & Mux
Sense Amplifier(s)
Burst Length (64B)
Target Word (8B)
Column Offset
Internal Ctrl.
1 Memory Transactions
1 Memory Transactions
2
3
4
5
6
7
8
2
Sense Amplifier(s)
Bandwidth Gain

## Slide 12
Piccolo-FIM: Scope of FIM Operation
If random accesses span multiple rows  unexpected activations
Restrict a random scatter/gather within an activated row
- Avoid unnecessary activation during operation
- Deterministic latency for the memory controller
Data Cell Array
DRAM w/ Piccolo-FIM
Internal Ctrl.
RD Buff.
WR Buff.
Column Decoder & Mux
Sense Amplifier(s)
Data Buffer
Offset Buffer

## Slide 13
Piccolo-FIM: Operation within DDR Standard
WRITE Offset Buffer
READ/WRITE Data Buffer
Gather/Scatter Execute
Data Cell Array
DRAM w/ Piccolo-FIM
Internal Ctrl.
RD Buff.
WR Buff.
Sense Amplifier(s)
Data Buffer
Offset Buffer
Column Decoder & Mux

## Slide 14
WRITE Offset Buffer
READ/WRITE Data Buffer
Gather/Scatter Execute
Piccolo-FIM: Operation within DDR Standard
WRITE Offset Buffer
READ/WRITE Data Buffer
Gather/Scatter Execute
Expose to Address Space
 Normal RD/WR Command
Data Cell Array
DRAM w/ Piccolo-FIM
Internal Ctrl.
RD Buff.
WR Buff.
Sense Amplifier(s)
Data Buffer
(Physical)
Offset Buffer
(Physical)
Row xx
Data Buffer (Virtual)
Offset Buffer (Virtual)
Column Decoder & Mux

## Slide 15
Expose to Address Space
 Normal RD/WR Command
WRITE Offset Buffer
READ/WRITE Data Buffer
Gather/Scatter Execute
WRITE Offset Buffer
READ/WRITE Data Buffer
Gather/Scatter Execute
Piccolo-FIM: Operation within DDR Standard
Data Cell Array
Internal Ctrl.
RD Buff.
WR Buff.
Sense Amplifier(s)
Row xx
Data Buffer (Virtual)
Offset Buffer (Virtual)
Column Decoder & Mux
Data Buffer
(Physical)
Offset Buffer
(Physical)
Need Multi-Col. Access Time
Adding new commands  Significant change in DDR Protocol

## Slide 16
WRITE Offset Buffer
READ/WRITE Data Buffer
Gather/Scatter Execute
WRITE Offset Buffer
READ/WRITE Data Buffer
Gather/Scatter Execute
Piccolo-FIM: Operation within DDR Standard
Data Cell Array
Internal Ctrl.
RD Buff.
WR Buff.
Sense Amplifier(s)
Column Decoder & Mux
Need Multi-Col. Access Time
Two Virtual DRAM Row
Use Activation Latency
Row xx
Data Buffer (Virtual)
Offset Buffer (Virtual)
Data Buffer
(Physical)
Offset Buffer
(Physical)
Row yy
Data Buffer (Virtual)
Offset Buffer (Virtual)

## Slide 17
Data Buffer
Piccolo-FIM: Operation within DDR Standard
Add two virtual rows (special addr.) to make activation (row xx ↔ yy)
Use activation latency to hide multi-column read latency
WR
BURST
ACT
RD
BURST
C/A Bus
Physical Access
Data Bus
WR Offset Buff.
GATHER (Multi-Column Access)
RD Data Buff.
[Row xx]
[Row yy]
Data Cell Array
Internal Ctrl.
RD Buff.
WR Buff.
Sense Amplifier(s)
Offset Buffer
Row xx
Data Buffer (Virtual)
Offset Buffer (Virtual)
Row yy
Data Buffer (Virtual)
Offset Buffer (Virtual)
Column Decoder & Mux
Precharge & Activation
RD
RD
RD
RD
RD
RD
RD
RD
WR
RD
Virtual Access

## Slide 18: Overview of Piccolo
Accelerator
Prefetcher
Processor
Updater
Vertex
Prefetch
Edge
Prefetch
PE
S
I
M
D
…
…
…
UE
RA Unit
Piccolo-Cache
l
l
Piccolo Function-in-Memory
Function-in-Memory Architecture
Operation within DDR Standard
(2) Piccolo Cache
Fine-Grained Cache Architecture
Collection-Extended MSHR
…
Offset Buffer
Data Cell Array
Piccolo Function-in-Memory
Ctrl.
Data Buffer

## Slide 19: Piccolo-Cache: Architecture
Gathered Data  Non-Contiguous Address Range
Conventional cache cannot manage it (cache line spans contiguous)
0x000
0x048
0x068
0x090
0x098
0x0f0
0x128
0x178
Data from Memory (64B):
Gathered Word
Address
Conventional Cache Line
Address
0x000
0x040
0x080
0x0c0
0x100
Data
0x140
64B
64B
64B
64B
64B
64B
8B
8B
8B
8B
8B
8B
8B
8B

## Slide 20: Piccolo-Cache: Architecture
Naïve solutions for managing data at 8B granularity
Need to consider both metadata overhead and performance
8B-Line Cache
Sectored Cache
8B
TAG
8B
TAG
8B
TAG
8B
TAG
8B
0x00
0x08
0x10
0x18
TAG
8B
0x00
0x08
0x10
0x18
TAG
8B
0x00
0x08
0x10
0x18
TAG
8B
TAG
-
-
-
-
-
-
-
-
-
-
-
-
tag for each 8B entry
Cacheline (64B) for 8B entry
Significant Performance Degradation
Significant Metadata Overhead

## Slide 21: Piccolo-Cache: Architecture
Set Index
Tag
FG Offset
Use the sectored cache structure w/ tag per line & fg-tag per sector
Allowing the same tag within a single set
Reduce metadata overhead: split {Tag}  {Tag + Fine-Grained Tag}
Tag
FG-Tag
Set Index
FG Offset

## Slide 22: Piccolo-Cache: Architecture
0x00
0x00
0x03
0x00
0x03
04
09
Each 8B data has a fg-tag and each 32B line has a tag
Evict a sector along with a fg-tag following LRU order
Set 0
Tag
FG-Tag
Set Index
FG Offset
<Request Addr>
0x03
0xff
Set 0
0x10
8B
FG-TAG
DATA
00
08
10
18
00
08
10
18
Way 0
Way 1
Way 2
Way 3
8B
8B
8B
8B
…
05
3f
1f
00
TAG
=
=
0x00
0x03
0x03
Hit!
04
09
Miss!
0x03
0xff
0x00
Miss!
ff
Multiple Tags
(LRU Evict)
Data Out
8B
Access Example (4-way, 4-sector)
LRU Order
0x10

## Slide 23: Piccolo-Cache: Collection-Extended MSHR
f0
xx
Piccolo
Cache
DRAM w/
Piccolo-FIM
Collection-Extended MSHR
...
...
Subentries
WB Data
Sequential Compare
Collect Controller
...
row xx
Bank 0
④ Send data
Conventional cache cannot send the collected memory request for Piccolo-FIM
Indexed by DRAM row addr., Issuing a collected request (e.g., in-memory gather)
SC-MSHR (collect writeback request), GA-MSHR (collect cache miss request)
...
...
...
SC-MSHR
GA-MSHR
Row
row xx
row yy
...
② Compare the request with existing offsets
18
28
8c
b0
...
...
...
① Cache miss incurs memory request
row yy
Bank １
③ Execute
Piccolo-FIM
...
2c
68
f0
00
e8
8 Col.
0c
38
40
5c
90
ac
00
e8
READ Addr.
Row xx
Col. f0
READ Addr.
Row xx
Col. 00
READ Addr.
Row xx
Col. e8

## Slide 24: Evaluation
Experimental Methodology
Microbenchmark
Evaluation Results
Introduction
Background
Motivations
Piccolo
Evaluation
Conclusion

## Slide 25: Experimental Methodology
3. Baselines
  GraphDyns: state-of-the-art
  NMP: rank-parallel scatter-gather
  PIM: in-memory computing
  Piccolo: host & FIM co-design
Objective | Component | Evaluation Method
Validation | Piccolo-FIM | FPGA Emulation
Performance | Overall | Simulation
Energy and Area | Accelerator Cache DRAM | RTL Synthesis CACTI Design Comparison
1. Method
2. Dataset
  5 large-scale graph dataset
  5 graph algorithms
  Use the best graph tiling config.
[Memory Config.]
DDR4x16, 2400R
1 channel, 4 ranks

## Slide 26: Evaluation: Speedup
1.62x over baseline (geomean)
PIM-only case is not enough
Significantly better performance (internal bandwidth and locality are well utilized)
Chart: Speedup
| UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | PR | BFS | CC | SSSP | SSWP | GM
GraphDyns (Cache) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NMP | 0.52347 | 0.90639 | 0.9019 | 1.1238 | 0.8982 | 0.65951 | 0.71744 | 1.128 | 1.7017 | 1.0806 | 0.52226 | 0.8378 | 1.2144 | 1.5104 | 1.1623 | 0.49393 | 0.62315 | 1.1972 | 1.9075 | 1.1784 | 0.46714 | 0.79428 | 1.1887 | 2.0075 | 1.287 | 0.96135
PIM | 0.59597 | 0.11791 | 0.82065 | 0.57971 | 0.5206 | 0.3909 | 0.15196 | 1.6663 | 1.3613 | 1.9178 | 0.60913 | 0.12021 | 1.5888 | 0.70419 | 0.98163 | 0.36198 | 0.14994 | 1.5678 | 0.61756 | 0.83859 | 0.35973 | 0.14525 | 1.5222 | 0.712 | 0.85315 | 0.56946
Piccolo | 1.5711 | 1.0424 | 1.5981 | 1.6923 | 1.3353 | 1.1055 | 1.4889 | 1.806 | 3.2801 | 1.7403 | 1.3483 | 1.1206 | 2.3763 | 1.9494 | 1.8473 | 1.1115 | 1.1219 | 2.3113 | 2.0978 | 1.7872 | 1.0988 | 1.0876 | 2.2142 | 2.2504 | 1.9239 | 1.6152
3.28x
1.62x

## Slide 27: Evaluation: Energy and Area
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | PR | BFS | CC | SSSP | SSWP
READ | 0.60249 | 0.35603 | 0.99139 | 0.85198 | 0.98532 | 0.40609 | 0.99423 | 0.41935 | 0.99278 | 0.63526 | 0.77417 | 0.63326 | 0.97757 | 0.39951 | 0.55638 | 0.3559 | 0.65505 | 0.18921 | 0.66856 | 0.36789 | 0.61947 | 0.47966 | 0.99048 | 0.67977 | 0.65806 | 0.23606 | 0.99383 | 0.28125 | 0.99459 | 0.35737 | 0.6774 | 0.50276 | 0.98749 | 0.64903 | 0.66895 | 0.24833 | 0.67198 | 0.27262 | 0.97636 | 0.38403 | 0.67012 | 0.49733 | 0.9812 | 0.66188 | 0.66174 | 0.24333 | 0.67571 | 0.27702 | 0.97198 | 0.38832
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | PR | BFS | CC | SSSP | SSWP
READ | 0.60249 | 0.35603 | 0.99139 | 0.85198 | 0.98532 | 0.40609 | 0.99423 | 0.41935 | 0.99278 | 0.63526 | 0.77417 | 0.63326 | 0.97757 | 0.39951 | 0.55638 | 0.3559 | 0.65505 | 0.18921 | 0.66856 | 0.36789 | 0.61947 | 0.47966 | 0.99048 | 0.67977 | 0.65806 | 0.23606 | 0.99383 | 0.28125 | 0.99459 | 0.35737 | 0.6774 | 0.50276 | 0.98749 | 0.64903 | 0.66895 | 0.24833 | 0.67198 | 0.27262 | 0.97636 | 0.38403 | 0.67012 | 0.49733 | 0.9812 | 0.66188 | 0.66174 | 0.24333 | 0.67571 | 0.27702 | 0.97198 | 0.38832
Chart: Normalized Energy
| Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | PR | BFS | CC | SSSP | SSWP
Acc. | 0.27727 | 0.17239 | 0.24411 | 0.23417 | 0.24497 | 0.14007 | 0.24467 | 0.13207 | 0.24477 | 0.16905 | 0.27336 | 0.24326 | 0.30122 | 0.1953 | 0.27154 | 0.14915 | 0.26692 | 0.077139 | 0.26654 | 0.1499 | 0.27636 | 0.20039 | 0.24242 | 0.20255 | 0.26145 | 0.10582 | 0.24521 | 0.11278 | 0.24576 | 0.1204 | 0.27483 | 0.24318 | 0.24471 | 0.20204 | 0.26106 | 0.10893 | 0.25551 | 0.10644 | 0.24506 | 0.12553 | 0.27519 | 0.24649 | 0.24467 | 0.20882 | 0.26118 | 0.11367 | 0.2551 | 0.11336 | 0.2468 | 0.12828
Cache | 0.34962 | 0.34631 | 0.49694 | 0.3733 | 0.46843 | 0.25709 | 0.47227 | 0.19946 | 0.47375 | 0.25922 | 0.35723 | 0.24584 | 0.32301 | 0.22293 | 0.30984 | 0.25181 | 0.33212 | 0.2215 | 0.33328 | 0.22448 | 0.35899 | 0.37268 | 0.49162 | 0.3374 | 0.35775 | 0.20564 | 0.47107 | 0.31871 | 0.46838 | 0.31557 | 0.36189 | 0.36189 | 0.48696 | 0.35973 | 0.361 | 0.19853 | 0.36941 | 0.16517 | 0.46619 | 0.19883 | 0.36194 | 0.25094 | 0.48684 | 0.37568 | 0.35892 | 0.2221 | 0.37138 | 0.1841 | 0.46173 | 0.20566
OTHERS | 0.081137 | 0.033679 | 0.040235 | 0.041308 | 0.040928 | 0.028175 | 0.040034 | 0.024411 | 0.040162 | 0.030488 | 0.072741 | 0.052974 | 0.055649 | 0.039111 | 0.091969 | 0.029574 | 0.08303 | 0.016153 | 0.082403 | 0.029146 | 0.078797 | 0.03773 | 0.039484 | 0.036189 | 0.077265 | 0.022514 | 0.040189 | 0.024633 | 0.040277 | 0.024246 | 0.076047 | 0.053047 | 0.040693 | 0.03841 | 0.076036 | 0.022375 | 0.075483 | 0.020079 | 0.041833 | 0.024263 | 0.076231 | 0.053912 | 0.041185 | 0.039785 | 0.07696 | 0.023395 | 0.074951 | 0.021295 | 0.042528 | 0.024704
DRAM RD | 0.032003 | 0.035184 | 0.0426 | 0.045222 | 0.047598 | 0.032647 | 0.047595 | 0.025993 | 0.04717 | 0.037518 | 0.043273 | 0.076365 | 0.061567 | 0.040544 | 0.032836 | 0.031762 | 0.038362 | 0.019086 | 0.039241 | 0.02955 | 0.032313 | 0.039782 | 0.044102 | 0.038959 | 0.0368 | 0.027545 | 0.047671 | 0.031106 | 0.048122 | 0.029948 | 0.035924 | 0.07604 | 0.044159 | 0.043326 | 0.037287 | 0.0249 | 0.0372 | 0.020591 | 0.047319 | 0.028157 | 0.035411 | 0.075819 | 0.043754 | 0.044483 | 0.03696 | 0.025022 | 0.037305 | 0.021046 | 0.04745 | 0.02844
DRAM WR | 0.032765 | 0.026677 | 0.00057405 | 0.01812 | 0.0011006 | 0.026983 | 0.00042854 | 0.011855 | 0.00053262 | 0.01546 | 0.019587 | 0.02114 | 0.0020337 | 0.035521 | 0.040626 | 0.026053 | 0.031347 | 0.015726 | 0.030187 | 0.021271 | 0.0308 | 0.02556 | 0.00065764 | 0.018285 | 0.029673 | 0.023972 | 0.00045919 | 0.027045 | 0.00040614 | 0.021003 | 0.026548 | 0.037209 | 0.00086842 | 0.028618 | 0.028634 | 0.024673 | 0.028178 | 0.01149 | 0.0017781 | 0.01971 | 0.027049 | 0.040516 | 0.0013008 | 0.030273 | 0.029317 | 0.026712 | 0.027781 | 0.012637 | 0.0021227 | 0.019889
DRAM I/O | 0.22721 | 0.12222 | 0.17554 | 0.17709 | 0.19697 | 0.12132 | 0.195 | 0.10035 | 0.19362 | 0.14634 | 0.23382 | 0.20973 | 0.25652 | 0.15008 | 0.2532 | 0.12367 | 0.24822 | 0.069662 | 0.24836 | 0.11828 | 0.22274 | 0.14431 | 0.18172 | 0.15153 | 0.23706 | 0.093567 | 0.1954 | 0.10138 | 0.19705 | 0.10535 | 0.22476 | 0.19994 | 0.1826 | 0.16284 | 0.23598 | 0.093391 | 0.23422 | 0.079259 | 0.19782 | 0.10611 | 0.22418 | 0.20195 | 0.18225 | 0.16728 | 0.23666 | 0.094908 | 0.23348 | 0.081601 | 0.19937 | 0.10764
37.3% less energy compared to baseline (geomean)
In-memory scatter-gather reduces memory transactions
4.10% area overhead for accelerator and 4.36% for memory chip
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | PR | BFS | CC | SSSP | SSWP
READ | 0.60249 | 0.35603 | 0.99139 | 0.85198 | 0.98532 | 0.40609 | 0.99423 | 0.41935 | 0.99278 | 0.63526 | 0.77417 | 0.63326 | 0.97757 | 0.39951 | 0.55638 | 0.3559 | 0.65505 | 0.18921 | 0.66856 | 0.36789 | 0.61947 | 0.47966 | 0.99048 | 0.67977 | 0.65806 | 0.23606 | 0.99383 | 0.28125 | 0.99459 | 0.35737 | 0.6774 | 0.50276 | 0.98749 | 0.64903 | 0.66895 | 0.24833 | 0.67198 | 0.27262 | 0.97636 | 0.38403 | 0.67012 | 0.49733 | 0.9812 | 0.66188 | 0.66174 | 0.24333 | 0.67571 | 0.27702 | 0.97198 | 0.38832
Chart: Normalized Energy
| Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | Conven. | Piccolo | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | UU | TW | SW | FS | PP | PR | BFS | CC | SSSP | SSWP
Acc. | 0.27727 | 0.17239 | 0.24411 | 0.23417 | 0.24497 | 0.14007 | 0.24467 | 0.13207 | 0.24477 | 0.16905 | 0.27336 | 0.24326 | 0.30122 | 0.1953 | 0.27154 | 0.14915 | 0.26692 | 0.077139 | 0.26654 | 0.1499 | 0.27636 | 0.20039 | 0.24242 | 0.20255 | 0.26145 | 0.10582 | 0.24521 | 0.11278 | 0.24576 | 0.1204 | 0.27483 | 0.24318 | 0.24471 | 0.20204 | 0.26106 | 0.10893 | 0.25551 | 0.10644 | 0.24506 | 0.12553 | 0.27519 | 0.24649 | 0.24467 | 0.20882 | 0.26118 | 0.11367 | 0.2551 | 0.11336 | 0.2468 | 0.12828
Cache | 0.34962 | 0.34631 | 0.49694 | 0.3733 | 0.46843 | 0.25709 | 0.47227 | 0.19946 | 0.47375 | 0.25922 | 0.35723 | 0.24584 | 0.32301 | 0.22293 | 0.30984 | 0.25181 | 0.33212 | 0.2215 | 0.33328 | 0.22448 | 0.35899 | 0.37268 | 0.49162 | 0.3374 | 0.35775 | 0.20564 | 0.47107 | 0.31871 | 0.46838 | 0.31557 | 0.36189 | 0.36189 | 0.48696 | 0.35973 | 0.361 | 0.19853 | 0.36941 | 0.16517 | 0.46619 | 0.19883 | 0.36194 | 0.25094 | 0.48684 | 0.37568 | 0.35892 | 0.2221 | 0.37138 | 0.1841 | 0.46173 | 0.20566
OTHERS | 0.081137 | 0.033679 | 0.040235 | 0.041308 | 0.040928 | 0.028175 | 0.040034 | 0.024411 | 0.040162 | 0.030488 | 0.072741 | 0.052974 | 0.055649 | 0.039111 | 0.091969 | 0.029574 | 0.08303 | 0.016153 | 0.082403 | 0.029146 | 0.078797 | 0.03773 | 0.039484 | 0.036189 | 0.077265 | 0.022514 | 0.040189 | 0.024633 | 0.040277 | 0.024246 | 0.076047 | 0.053047 | 0.040693 | 0.03841 | 0.076036 | 0.022375 | 0.075483 | 0.020079 | 0.041833 | 0.024263 | 0.076231 | 0.053912 | 0.041185 | 0.039785 | 0.07696 | 0.023395 | 0.074951 | 0.021295 | 0.042528 | 0.024704
DRAM RD | 0.032003 | 0.035184 | 0.0426 | 0.045222 | 0.047598 | 0.032647 | 0.047595 | 0.025993 | 0.04717 | 0.037518 | 0.043273 | 0.076365 | 0.061567 | 0.040544 | 0.032836 | 0.031762 | 0.038362 | 0.019086 | 0.039241 | 0.02955 | 0.032313 | 0.039782 | 0.044102 | 0.038959 | 0.0368 | 0.027545 | 0.047671 | 0.031106 | 0.048122 | 0.029948 | 0.035924 | 0.07604 | 0.044159 | 0.043326 | 0.037287 | 0.0249 | 0.0372 | 0.020591 | 0.047319 | 0.028157 | 0.035411 | 0.075819 | 0.043754 | 0.044483 | 0.03696 | 0.025022 | 0.037305 | 0.021046 | 0.04745 | 0.02844
DRAM WR | 0.032765 | 0.026677 | 0.00057405 | 0.01812 | 0.0011006 | 0.026983 | 0.00042854 | 0.011855 | 0.00053262 | 0.01546 | 0.019587 | 0.02114 | 0.0020337 | 0.035521 | 0.040626 | 0.026053 | 0.031347 | 0.015726 | 0.030187 | 0.021271 | 0.0308 | 0.02556 | 0.00065764 | 0.018285 | 0.029673 | 0.023972 | 0.00045919 | 0.027045 | 0.00040614 | 0.021003 | 0.026548 | 0.037209 | 0.00086842 | 0.028618 | 0.028634 | 0.024673 | 0.028178 | 0.01149 | 0.0017781 | 0.01971 | 0.027049 | 0.040516 | 0.0013008 | 0.030273 | 0.029317 | 0.026712 | 0.027781 | 0.012637 | 0.0021227 | 0.019889
DRAM I/O | 0.22721 | 0.12222 | 0.17554 | 0.17709 | 0.19697 | 0.12132 | 0.195 | 0.10035 | 0.19362 | 0.14634 | 0.23382 | 0.20973 | 0.25652 | 0.15008 | 0.2532 | 0.12367 | 0.24822 | 0.069662 | 0.24836 | 0.11828 | 0.22274 | 0.14431 | 0.18172 | 0.15153 | 0.23706 | 0.093567 | 0.1954 | 0.10138 | 0.19705 | 0.10535 | 0.22476 | 0.19994 | 0.1826 | 0.16284 | 0.23598 | 0.093391 | 0.23422 | 0.079259 | 0.19782 | 0.10611 | 0.22418 | 0.20195 | 0.18225 | 0.16728 | 0.23666 | 0.094908 | 0.23348 | 0.081601 | 0.19937 | 0.10764

## Slide 28: Evaluation: Microbenchmark
Piccolo-FIM FPGA Emulation
Validation Test with Microbenchmark (Stride Access)
Achieve Almost Ideal Speedup (4x)
Chart: Stride
| 4 | 8 | 16 | 32
Conventional | 1 | 1 | 1 | 1
Piccolo | 1.7285 | 3.6149 | 3.6128 | 3.6105

## Slide 29: Conclusion
Piccolo  Accelerator & FIM Co-Design
Low Overhead & Minimal Change to DRAM
End-to-End Graph Processing Accelerator
  In-Memory Random Scatter-Gather
  Fine-Grained Cache Architecture
  Collection-Extended MSHRs

## Slide 30: Thank you.
Changmin Shin @ Seoul National University
Email: scm8432@snu.ac.kr